## Slide 1: Course Project
Mohab Hassan

## Slide 2: Introduction
int x = 2;
int y = 3;
int z = y/x; // z = 1
float x = 2.0;
float y = 3.0;
float z = y/x;// z = 1.5f
Runs on ALU
Runs on FPU

## Slide 3: Scientific Notation
Any number (in base-10) can be represented as:
Where, s: sign bit (0 or 1)
d: single digit
m: mantissa
e: exponent
Decimal notation | Scientific notation
2 | 2×100
300 | 3×102
4321.768 | 4.321768×103
−53000 | −5.3×104
6720000000 | 6.72×109
0.2 | 2×10−1
987 | 9.87×102
0.00000000751 | 7.51×10−9

## Slide 4: Scientific Notation - Normalization
Denormalized | Normalized
30×101 | 3×102
43.21768×102 | 4.321768×103
−530.00×102 | −5.3×104
6720000000 | 6.72×109
0.02×101 | 2×10−1

## Slide 5: Floating Point Notation
Similar to scientific notation, FP (in base 2) notation is:
Where, s: sign bit
m: mantissa
e: exponent
the digit to the left of the decimal point is always 1 (except for special values).
Numbers should always be normalized.
Decimal notation | Floating point notation
1 | (-1) 0×1.0×20
300 | (-1) 0×1.171875×28
4321.768 | (-1) 0×1.0551191568374634×212
−53000 | (-1) 1×1.617431640625×215
6720000000 | (-1) 1×1.564621925354004×232
0.2 | (-1) 0×1.600000023841858×2-3
987 | (-1) 0×1.927734375×29
0.00000000751 | (-1) 0×1.0079751014709473×2-27

## Slide 6: Floating Point Notation - Binary
Similar to scientific notation, FP (in base 2) notation is:
For single precision float(32bit)
s: sign bit (1 bit)
m: mantissa (23 bits)
e: exponent (8 bits)
Single precision floating point representation of 300 300 = (-1) 0×1.171875×28 300 = (-1) 0×(1.00101100000000000000000)2×28 |  | 
31 | 30:23 | 22:0
s | e | m
0 | 00001001 | 00101100000000000000000

## Slide 7: Floating Point Notation - Binary
Similar to scientific notation, FP (in base 2) notation is:
For double precision float(64bit)
s: sign bit (1 bit)
m: mantissa (52 bits)
e: exponent (11 bits)
Double precision floating point representation of 300 300 = (-1) 0×1.171875×28 300 = (-1) 0×(1.00101100000000000000000)2×28 |  | 
63 | 62:52 | 51:0
s | e | m
0 | 00000001001 | 0010110000000000000000000000000000000000000000000000

## Slide 8: Floating Point Notation - Biasing
where E= 127+e for SP
Biasing is introduced to make life easier in comparisons and other operations.
Single precision floating point representation of 300 300 = (-1) 0×1.171875×28 300 = (-1) 0×(1.00101100000000000000000)2×2135 |  | 
31 | 30:23 | 22:0
s | E | m
0 | 10000111 | 00101100000000000000000

## Slide 9: Floating Point Notation - Biasing
where E= 1023+e for DP
Biasing is introduced to make life easier in comparisons and other operations.
Double precision floating point representation of 300 300 = (-1) 0×1.171875×28 300 = (-1) 0×(1.00101100000000000000000)2×21031 |  | 
63 | 62:52 | 51:0
s | E | m
0 | 10000000111 | 0010110000000000000000000000000000000000000000000000

## Slide 10: Floating Point Operations – Multiplication
Suppose we want to multiply 2 numbers, A, and B, where:

## Slide 11: Floating Point Operations - Addition
Suppose we want to add 2 numbers, A, and B, where:

## Slide 12: Floating Point Special Numbers
The following are special numbers in SP floating point representation.
Single precision floating point representation of various special values | Single precision floating point representation of various special values |  | 
 | 31 | 30:23 | 22:0
Number | s | E | m
+0 | 0 | 00000000 | 00000000000000000000000
-0 | 1 | 00000000 | 00000000000000000000000
NaN | X | 11111111 | 1XXXXXXXXXXXXXXXXXXXXXX
+inf | 0 | 11111111 | 00000000000000000000000
-inf | 1 | 11111111 | 00000000000000000000000

## Slide 13: Floating Point Special Numbers
Both +0 and -0 are equal
NaN happens when:
  Input of operation has NaN
  0/0, inf/inf, 0*inf, inf - inf, x%0, inf%x
  Output of operation is a complex number
Inf happens when:
  Input of operation has inf (except for NaN cases above)
  x/0, where x is not 0
  Exponent overflow

## Slide 14: Floating Point Operations Algorithm
  Check for special numbers and output accordingly, otherwise continue
  Perform addition/multiplication
  Normalize result
  Check for overflow/underflow

## Slide 15: Project Requirement
Implement a SP and DP FP Unit where supported operations are:
00 FP addition
01 Subtraction
10 Multiplication
11 Unused
Should contain: FP Adder, FP Multiplier
Parameters should be used with the code to change between SP and DP implementation
Handle overflows/underflows and special numbers (zero, inf, NaN)
Comprehensive test benches for all the test cases and edge cases (special numbers, overflow, etc…) should be made for each module and submodule.

## Slide 16: Important Notes
For all requirements and the project, we expect your work to be original.
Cheating will not be tolerated.
If you have questions, feel free to ask me:
  mohabhassan365@gmail.com
  t.me/mohabhassan365
Feel free to contact Eng. Loay:
  loayhamed99@gmail.com